## Slide 1
WEARABLE ASSISTIVE TECH
◉
ESP32-S3 · I2C · BLE
VLS 603 — ELECTRONIC SYSTEMS PACKAGING
Navigator Band
Haptic Obstacle Guidance for the Visually Impaired
Swayam Kotecha | ESP32-S3 · 4 Sensors · Dual Haptic Motors
SLIDE 1 / 8

## Slide 2
THE PROBLEM
253 million visually impaired people worldwide
CURRENT SOLUTIONS
White cane
no real-time obstacle alerts
Phone audio
phone must stay out of pocket
Chest devices
bulky, socially very visible
OUR SOLUTION
Wristband form factor
socially invisible, always with you
Haptic + audio output
no visual needed, phone stays pocketed
Fully self-contained
no phone, no app, no internet required
SLIDE 2 / 8

## Slide 3
SYSTEM ARCHITECTURE
Four functional blocks on one PCB
POWER BLOCK
USB-C
MCP73831
XC6206 LDO
LiPo 400mAh
3.3V rail
MCU BLOCK
ESP32-S3
BLE 5.0
I2C Master
I2S Audio
3.3V logic
SENSOR BLOCK
VL53L1X (ToF)
ICM-42688 (IMU)
VEML7700 (Light)
MAX30205 (Temp)
I2C bus shared
FEEDBACK BLOCK
DRV2605L(Haptic)
2× LRA Motors
MAX98357 Amp
Micro Speaker
Haptic + Audio
SLIDE 3 / 8

## Slide 4
SENSOR SUITE
Four sensors, four purposes
①
VL53L1X — Time of Flight
Fires infrared laser 50×/sec · measures distance 0–4m · primary obstacle sensor
②
MPU9250 — IMU
Accelerometer + gyroscope · corrects ToF readings for wrist tilt · counts footsteps
③
VEML7700 — Ambient Light
Measures lux level · switches polling rate indoors vs outdoors · saves battery
④
MAX30205 — Skin Temperature
Reads skin surface temp · detects if device is worn · triggers deep sleep when removed
SLIDE 4 / 8

## Slide 5
40X36

## Slide 7
Power manag
ESP-32
Lin reg(3.7->3.3)
Haptic
Light sensor
Tof
Temp
IMU sensor

## Slide 8
Light sensor
IMU
ESP-32
Haptic
ToF sensor
audio

## Slide 9
Body Temp sensor(in contact with skin)

## Slide 10
HOW IT WORKS
Step-by-step obstacle response pipeline
Boot
Skin temp check 3 buzz startup All sensors init
→
ToF Fires
Laser pulse sent Distance measured 50 times/sec
→
IMU Check
Wrist angle verified Ignore if pointing at floor
→
Alert Level
<50cm strong buzz <100cm double pulse <150cm slow pulse
→
Feedback
Haptic motors fire Audio: Move right Left/right motors differ
SLIDE 5 / 8

## Slide 11
FEEDBACK DESIGN
Haptic grammar + pre-loaded audio cues
VIBRATION PATTERNS — DRV2605L
> 150 cm
No vibration — clear path
80–150 cm
Slow single pulse — caution
30–80 cm
Fast double pulse — slow down
< 30 cm
Strong continuous buzz — STOP
AUDIO CUES — MAX98357 + SPEAKER
left.wav
"Turn Left"
Obstacle detected on the right side
right.wav
"Turn Right"
Obstacle detected on the left side
stop.wav
"Stop!"
Obstacle closer than 30 cm — halt
All clips stored in ESP32-S3 flash memory · ~20 KB each · fully offline
SLIDE 7 / 8

## Slide 12
POWER ARCHITECTURE
USB-C charging · single clean 3.3V rail
INPUT
USB-C — 5V
↓
CHARGER IC
MCP73831
↓
STORAGE
LiPo 400mAh (3.7V nominal)
↓
REGULATOR
XC6206 LDO → 3.3V
3.3V Rail → ESP32-S3 · All 4 Sensors · DRV2605L · MAX98357
Skin temp drops → device removed → full system enters deep sleep
SLIDE 6 / 8
Skin temp drops → device removed → full system enters deep sleep

## Slide 13
KICAD DELIVERABLES
What we design and submit
01
Power
USB-C, MCP73831, XC6206 LDO, LiPo connector
02
MCU
ESP32-S3 module, all pin labels, decoupling caps
03
Sensors
All 4 sensor ICs, I2C bus, 4.7kΩ pull-up resistors
04
Feedback
DRV2605L haptic driver, MAX98357 amp, connectors
PCB LAYOUT — 2 LAYER · 40x36 mm
Ground plane
Full bottom copper pour, all GND nets connected
DRC clean
Zero errors · 3D view generated · Gerbers exported
Bill of Materials
Part numbers, package sizes, footprints all listed
Self-contained · No app · No GPS · Fully demonstrable in classroom
VLS 603 · Navigator Band
SLIDE 8 / 8
ERC clean
Zero errors · Zero Warnings